## Slide 1
Quantified Tree Risk Assessment Limited, UK
www.qtra.co.uk
QTRA Illustrated Example No. 1
To be viewed as a slide show
Licensed User example 01-08
VALUING LAND USE FOR ONE-OFF EVENTS AND VALUING LAND USE PER SQUARE METRE

## Slide 2: One-off Event Occupation Rates
This example seeks to demonstrate how variable occupation of a footpath over a year is summed to provide a probability of occupation at any point in the year.
When we value human occupation, we consider it as total available time -3,600 seconds per hour, 86,400 seconds per day, 8,760 hours per year and so on- divided by the total occupation. E.g. one pedestrian per day = 5 seconds/86,400 seconds = probability of occupation 1/17,280.
Example
  A mature tree is located on a parkland site and for 364 days of the year a daily average of two pedestrians per day pass beneath the tree, which comprises Mrs Jones taking her usual route to walk her dog in and out of the park
  2 x 364 days = 728 pedestrians for 364 days of the year
  For one day in August each year there is a flower show in the park when park access is diverted and 15,000 people each pass twice beneath the tree, which gives an occupation of 30,000 pedestrian movements for that day

## Slide 3: One-off Event Occupation Rates
30,728
= 84.19 movements per day (average)
365
The average occupation over the year which will be used in the risk assessment is calculated below
= Probability of Occupation 1/205 (Target 3)
728 Mrs Jones occupation (movements) over 364 days
+ 30,000 Pedestrian movements on the day of the show
= 30,728 Total movements for the year
84.19 x 5 seconds = 421 seconds occupation per day
421 1
86,400 205
=

## Slide 4: Valuing Targets by Area
Annual occupation of 100 Children and staff
x 150 days per year x 1 hour per day = 15,000 hours
occupied per year
School Playground
1,200m2
1.71 (people) x £1,000,000 = £1,710,000 value for the whole playground £1,710,000 ÷ 1,200m2 (area of playground) = £1,425 per m2
=
1.71/1 (constant occupation by 1.71 people)
=
15,000 hours occupied per year
8,760 actual hours per year
1.71
1
=
Using the Value of Statistical Life of £1,000,000 we convert the human targets to a per square metre monetary value
The red example considers the value of the target associated with whole tree failure having a footprint of 50m2
50m2
Red example – whole tree failure
Area of 50m2 x £1,425 per metre = £71,250
71,250 = 1
1,000,000 14
`
12m2
Yellow example – branch failure
Area of 12m2 x £1,425 per metre = £17,100
17,100 = 1
1,000,000 58
The yellow example considers the value of the target associated with a single branch having a footprint of 12m2

## Slide 5: www.qtra.co.uk